## Slide 1: University of Nottingham FYP Presentation
March 2024

## Slide 2: Goal: Classification of Emotions using Heart Signals on ARM Cortex-M

## Slide 3: Comparison Between ARM Processors
Features | Cortex-A | Cortex-R | Cortex-M
Instruction Set Architecture | ARM | ARM | Thumb
Instruction bits | 32 | 32 | 32
FPU | Yes | Yes | Optional
DSP Instruction | Yes | Yes | Yes (M4)
Dynamic Power |  |  | 
Application | High Performance | Real-Time | Embedded
Features | Cortex-A | Cortex-R | Cortex-M
Instruction Set Architecture | ARM | ARM | Thumb
Instruction bits | 32 | 32 | 32
FPU | Yes | Yes | Optional
DSP Instruction | Yes | Yes | Yes (M4)
Dynamic Power |  |  | 
Application | High Performance | Real-Time | Embedded

## Slide 4: Setting Up STM32CubeIDE & Testing Code
Requirements
5V 3A power supply is needed
ST-Link used as a debugger connection
Engineering Mode/Boot Mode

## Slide 5: Setting Up STM32CubeIDE & Testing Code

## Slide 6: Connecting ECG sensors onto STM32MP157F-DK2
void setup() {
Serial.begin(9600);
pinMode(10, INPUT); // Setup for leads off detection LO +
pinMode(11, INPUT); // Setup for leads off detection LO -
}
void loop() {
if((digitalRead(10) == 1)||(digitalRead(11) == 1)){
Serial.println('!');
}
else{
// send the value of analog input 0:
Serial.println(analogRead(A0));
}
//Wait for a bit to keep serial data from saturating
delay(1);
}

## Slide 7: Connecting ECG sensors onto STM32MP157F-DK2

## Slide 8: Problems

## Slide 9: STM32 Pin Configuration
ADC
LO-
LO+
ST-Link UART

## Slide 10: ADC

## Slide 11: Problem

## Slide 12: UART

## Slide 13: Problems

## Slide 14: Problems

## Slide 15: Code – Printing ADC values via ST-Link
while (1)
{
  HAL_ADC_Start(&hadc2);
  HAL_ADC_PollForConversion(&hadc2, HAL_MAX_DELAY);
  raw = HAL_ADC_GetValue(&hadc2);
  HAL_Delay(10);
  sprintf(msg, "%d\r\n", raw);
  HAL_UART_Transmit(&huart4, msg, strlen(msg), HAL_MAX_DELAY);
  }

## Slide 16: Code – Printing ADC values via ST-Link
__HAL_RCC_VREF_CLK_ENABLE(); // Enable the VREF clock
HAL_SYSCFG_VREFBUF_HighImpedanceConfig(SYSCFG_VREFBUF_HIGH_IMPEDANCE_DISABLE); // Disable the high impedance mode which is the default one read page 1694 of refman
HAL_SYSCFG_VREFBUF_VoltageScalingConfig(SYSCFG_VREFBUF_VOLTAGE_SCALE1); // To set the volage to 2.5v
HAL_SYSCFG_EnableVREFBUF(); // To enable VREFBUF
if(HAL_ADCEx_Calibration_Start(&hadc2, ADC_CALIB_OFFSET_LINEARITY, ADC_SINGLE_ENDED) != HAL_OK)
{
/* Calibration Error */
Error_Handler();
}

## Slide 17: Result
https://youtu.be/zIlDBF6tEII

## Slide 18: Wearable Design – Reference

## Slide 19: Wearable Design – Clip on Pants

## Slide 20: Initial Idea – Emotion Recognition
CNN
Image data
Use a combined dataset
(WESAD, AMIGOS, DREAMER, DEAP)
Fine tune model to deploy
https://www.eecs.qmul.ac.uk/mmv/datasets/amigos/download.html
https://zenodo.org/records/546113#.YKLY0WYzaHs
https://zenodo.org/records/546113#.YKLY0WYzaHs
https://archive.ics.uci.edu/dataset/465/wesad+wearable+stress+and+affect+detection

## Slide 21: Initial Idea – Emotion Recognition

## Slide 22: Initial Idea – Emotion Recognition

## Slide 23: Emotion Recognition
Sequential Neural Network
Raw 16-bit data
1 seconds frame (approximately 500Hz)
WESAD dataset
Build everything from scratch

## Slide 24: WESAD Dataset

## Slide 25: Dataset Validation before Preprocessing

## Slide 26: Dataset Preprocessing
import pickle
import pandas as pd
import numpy as np
# Load data from the pickle file
with open("data_preprocessing\\pkl_data\\S17.pkl", "rb") as file:
obj = pickle.load(file, encoding="latin1")
# Extract 'label' and 'ECG' arrays
label_data = obj['label']
ecg_data = obj['signal']['chest']['ECG']
# Create a DataFrame with 'label' and 'ECG' columns
df = pd.DataFrame({'label': label_data.flatten(), 'ECG': ecg_data.flatten()})
# Filter out rows where the label is 1, 5, 6, or 7
filtered_df = df[~df['label'].isin([0, 5, 6, 7])].copy() # Make a copy to avoid SettingWithCopyWarning
# Create a '16-bit' column based on the modified formula using .loc
filtered_df.loc[:, '16-bit'] = ((filtered_df['ECG'] / 3) + 0.5) * (2 ** 16)
# Reshape 'label' and '16-bit' arrays to have the same number of rows
num_rows = len(filtered_df) // 7000 * 7000
label_data = filtered_df['label'][:num_rows].values.reshape((-1, 7000))
bit16_data = filtered_df['16-bit'][:num_rows].values.reshape((-1, 7000))
# Identify rows where labels differ within the 7000 readings and discard those rows
valid_rows_mask = (label_data == label_data[:, [0]]).all(axis=1)
label_data = label_data[valid_rows_mask]
bit16_data = bit16_data[valid_rows_mask]
# Create a DataFrame with transposed '16-bit' data
final_df = pd.DataFrame(np.hstack((bit16_data, label_data[:, 0].reshape(-1, 1))), columns=[f'data{i+1}' for i in range(7000)] + ['label'])
# Save the final DataFrame to CSV
final_df.to_csv("data_preprocessing\\output_filter_label\\output_S17.csv", index=False)
Last Col: Label
16-bit ECG

## Slide 27: Dataset Validation after Preprocessing

## Slide 28: Dataset Validation after Preprocessing
https://colab.research.google.com/drive/1GXLzKMqylWgAKi7cYG9Fpy2-18rGqPAd#scrollTo=QM67ZIECR2rb

## Slide 29: Model Result – Overfits!

## Slide 30: Conversion of TensorFlow to TFLite

## Slide 31: X-Cube-AI Installation

## Slide 32: X-Cube-AI Installation

## Slide 33: Flash memory not enough!

## Slide 34: Fine tuning…

## Slide 35: Complexity Reduction!
Initial Output Overfits:
Reduce to stress & non-stress classification (2 output classification)
Reduce to 5000 inputs (approx. 500Hz)
Restart the whole process from data preprocessing

## Slide 36: Complexity Reduction!
Less Overfits:

## Slide 37: Enough Flash & RAM after Medium compression!

## Slide 38: Setup model in ARM Cortex-M4

## Slide 39: Library Depreciated

## Slide 40: Solution
https://wiki.st.com/stm32mcu/wiki/AI:How_to_perform_motion_sensing_on_STM32L4_IoTnode

## Slide 41: Debugging…

## Slide 42: Solution

## Slide 43: Solution

## Slide 44: Success!

## Slide 45: What’s Next?